## Slide 1: ROS-Based UAV Flight Control and Collision Avoidance
Matt Holt

## Slide 2: This Presentation
Covers:
  What is ROS?
  ROS Concepts
  Our current ROS implementation
Doesn’t cover:
  ROS Install (Google it!)
  Specific ROS syntax (Google it!)

## Slide 3: What is ROS?
Robot Operating System (ROS), more like a framework than an OS
Library of component intended for robot applications
Many standard components for devices on robots
Simplified methods of:
  Multi-process applications
  Communication standards
Primarily runs C++ and Python on Ubuntu, Mac OS X functionality is mostly there also
Webpage: http://www.ros.org/wiki/
Example of Kinect mounted on Roomba: http://www.ros.org/wiki/Robots/TurtleBot

## Slide 4: The Node – ROS Concepts
Thought of as a process
Performs a specific task
Must register with the master process (roscore)
Many Nodes form a single application

## Slide 5: Topics – ROS Concepts
Much like a bulletin board, many-to-many
Messages are posted to it
Publishers
  Post TO the topic
  May have many or none
Subscribers
  Reads FROM the topic
  Typically has a callback for when a message is received
  May have many or none
Once declared a publisher or subscriber, ROS handles all communication channels

## Slide 6: Services – ROS Concepts
One-to-one communication
Request/response communication
Also has a callback to some function
Generally used for one-time functions or things requiring a response
Nodes advertise services for other nodes to use

## Slide 7: Useful ROS Commands
rosmake – like “make” only it performs additional tasks such as creating the headers for messages and services
roscore – necessary to be running in order to use other ROS components
rosrun – used to run a specific component
roslaunch – will launch multiple components along with roscore
rxgraph – displays a graphical menu much like…

## Slide 8: Example From ROS

## Slide 9: AU_UAV_ROS
The ROS package we created
Major Components:
  X-Bee IO
  Simulator
  Coordinator
  User Menu
Components for you:
  Collision Avoidance
  Visualization

## Slide 10: In the beginning…
X-Bee IO

## Slide 11: X-Bee IO – Component
Original JAVA code from last summer
Ported into ROS framework
Responsible for:
  X-Bee communication
  Translation from internal data to a message understood by the ArduPilot and vice versa

## Slide 12: Post it
X-Bee IO
Telemetry Updates

## Slide 13: Telemetry Updates – Topic
Topic consisting of information sent FROM a UAV
Types of information:
  Plane ID
  Position (Latitude, Longitude, Altitude)
  Destination (Lat., Long., Alt.)
  Speed
  Bearing

## Slide 14: Read it
X-Bee IO
Telemetry Updates
Coordinator

## Slide 15: Coordinator – Component
Primarily in charge of monitoring the planes and communicating the next destination of a plane
Responsibilities:
  Detect when a plane has reached a destination
  Sending next destination (whether it’s a true destination or avoidance destination)
  Alerting planes to collision avoidance maneuvers

## Slide 16: Where do we go now?
X-Bee IO
Telemetry Updates
Coordinator
Commands

## Slide 17: Commands – Topic
Topic for sending new commands to a UAV
ONLY the coordinator updates this topic, I would prefer to keep it this way if possible
Types of information:
  Plane ID of recipient
  Waypoint index
  New Destination (Lat., Long., Alt.)

## Slide 18: If you can dodge a wrench…
X-Bee IO
Telemetry Updates
Coordinator
Commands
Collision Avoidance

## Slide 19: Collision Avoidance – Component
In charge of monitoring UAV position to avoid collisions
Responsibilities:
  UAV monitoring
  Report avoidance maneuvers to Coordinator
How it works is up to you!
If you need special information or a way to report a maneuver for a particular algorithm/system, let me know and we’ll see what we can do

## Slide 20: Real fake
X-Bee IO
Telemetry Updates
Coordinator
Commands
Collision Avoidance
Simulator

## Slide 21: Simulator – Component
Responsible for simulating a UAV
Very basic simulation this summer
Potential room for extra work here
Responsibilities
  Sending simulated updates
  Receiving commands and changing “trajectory” accordingly
  Detecting a “crash”

## Slide 22: Nothing like HD
X-Bee IO
Telemetry Updates
Coordinator
Commands
Collision Avoidance
Simulator
Visualization

## Slide 23: Visualization – Component
Optional for you guys
This component would visualize the UAV positions on a map or something similar
Responsibilities:
  Receiving new telemetry
  Displaying the position/path of the UAV
  Looking awesome

## Slide 24: How do I do it?
X-Bee IO
Telemetry Updates
Coordinator
Commands
Collision Avoidance
Simulator
Visualization
Control Menu

## Slide 25: Control Menu – Component
Service based component for creating planes and load paths
Responsibilities:
  Provide a UI for managing the system as a whole
  Ability to create simulated planes
  Ability to load single waypoints or paths
  Ability to load courses (aka, multiple planes)

## Slide 26: Final Product – Questions?
X-Bee IO
Telemetry Updates
Coordinator
Commands
Collision Avoidance
Simulator
Visualization
Control Menu